R Series

Furnish and install as shown on the plans “R” Series round top enclosures with elements, required mounting components and all accessories as manufactured by Slant/Fin Corporation.

Cover shall be of one piece construction. Enclosure shall be (RL-10, RT-14, RT-21 or RT-28) and shall have (1, 2 or 3) tier element. (A knob actuated damper shall be provided.) Top part of enclosure shall consist of stamped grille with pencil-proof air discharge louvers.  All enclosures shall have female-to-female slip joint connection with interlocking internal splice. The internal splice provides additional strength with a nearly invisible joint. (Optional: A full height back panel shall be provided of 20-gauge electro galvanized steel finish.)

(Optional: Cover with anodized aluminum grill in place of pencil proof louvers. Cover shall be fabricated from 18 (16 or 14) gauge galvanized steel. Cover finish shall be galvanized or powder coated to a color as per specification. Brackets and hangers shall have a galvanized finish. Cover panels shall join using slip joint resulting in a clean and neat joint. (Please note damper is not available with anodized aluminum grill cover.)

Cover shall be fabricated from 18 (16 or14) gauge steel in hot dipped wiped coat galvanized finish or as custom color matched as per specification. Brackets and hangers shall be channeled steel  in hot dipped wiped coat galvanized finish. Fin-tube element(s) shall be Model___________. Provide lengths and capacities as scheduled on plans.

Furnish required channeled bracket-hanger assemblies with heavy flag brace for rigid front skirt and element support.  Provide all required accessories for a complete installation. Enclosure accessories in electro galvanized steel shall be telescopic and match enclosure color.